## Slide 1
Beam
Reaction, shear force, and bending moment
Stress and Strain
Deflection curve
Chapter 6.1-6.6, 6.9-6.10; 7.1-7.4; 12; 14.2; 14.10
Mechanics of Materials

## Slide 2: Engineering Structures

## Slide 3
Nanotechnology

## Slide 4
Biotechnology

## Slide 5
Beam in Bending
Deflection
Reaction
Strain
Stress

## Slide 6: Types of Supports and Reactions
Roller support:
Vertical displacement forbidden
Vertical reaction force
Pin support:
Vertical/lateral displacement forbidden
Vertical/lateral reaction force
Fixed support:
Vertical/lateral displacement forbidden
Vertical/lateral reaction force
Rotation forbidden
Reaction moment

## Slide 7: Free Body Diagram and Equilibrium
Simply supported beam
Cantilever beam
Simply supported beam
with overhang

## Slide 8: Shear Force & Bending Moment

## Slide 9: Deformation Sign Convention

## Slide 10: Shear Force & Bending Moment Diagram
Negative q
Negative P
Positive M0
Sign of q, P, and M determined by static sign convention
Sign of V determined by deformation sign convention

## Slide 11: Uniformly Distributed Load

## Slide 12: Three-Point Bending

## Slide 13: Shear Force & Bending Moment Diagram
Calculate reaction forces and moments at the supports
Draw shear force diagram first
  Identify the shear force at origin, based on the reaction force at the left support, with its sign by deformation convention
  Draw linear curve, with slope given by q, unless encounter a concentrated load
  At the point of concentrate load, have a jump in shear force;
  Check consistency at the right support
Draw bending moment diagram next
  Identify the bending moment at the origin, based on reaction moment at the left support; deformation sign convention
  Draw moment with slope given by V from shear force diagram
  At the point of concentrate moment, have a jump
  Check consistency at the right support

## Slide 14: Three- & Four-Point Bending
What is the difference?

## Slide 15: Shear Force and Bending Moment Diagram
What is RA, RB?

## Slide 16: Shear Force and Bending Moment Diagram
Where, and what is maximum M?

## Slide 17: Quiz

## Slide 18: Deflection in Beam

## Slide 19: Normal Stress in Beam
How to identify the neutral axis?

## Slide 20: Normal Stress
Go through centroid !

## Slide 21
Three- & Four-Point Bending
How stress is varied?

## Slide 22
Example
What is bending moment?

## Slide 23
I Beam
Why?

## Slide 24
Example

## Slide 25
Parallel Axis Theorem

## Slide 26
Example

## Slide 27
Example

## Slide 28
Example
Origin on the top

## Slide 29: Shear Stress
Magnitude only
Origin at centroid

## Slide 30: Distribution of Shear Stress

## Slide 31: Shear Stress

## Slide 32: Shear Stress

## Slide 33: Example
Shear stress at P and maximum shear?

## Slide 34: Example

## Slide 35: Example

## Slide 36: Example
Maximum shear

## Slide 37: Example
Origin at bottom

## Slide 38: Example

## Slide 39: Three- & Four-Point Bending
What is the difference?

## Slide 40: Plastic Bending

## Slide 41: Plastic Bending

## Slide 42: Fully Plastic

## Slide 43: Deflection of Beam

## Slide 44: Deflection of Curve

## Slide 45: Boundary Condition

## Slide 46: Continuity Condition

## Slide 47: Deflection by Bending Moment Equation

## Slide 48: Deflection by Loading Equation

## Slide 49: Three-Point Bending
Slope at x=a
Deflection at x=a
Deflection at x=L

## Slide 50: Three-Point Bending
a=b:
middle

## Slide 51: Deflection by Superposition

## Slide 52: Four-Point Bending
a
b
b
a
x
(1)
(2)

## Slide 53: Bonus Quiz
P
a
Determine deflection curve

## Slide 54
2.73 N/m
69.7 kHz
AFM Cantilever

## Slide 55: What If?

## Slide 56: Strain Energy of Pure Bending

## Slide 57: Strain Energy of Bending

## Slide 58: Strain Energy of Bending

## Slide 59: Example

## Slide 60: Example

## Slide 61: Castigliano’s Theorem
When forces act on a elastic system
subject to small displacements, the
displacement corresponding to any
force, collinear with the force, is equal
to the partial derivative of the total
strain energy with respect to that force.

## Slide 62: Application
Left half

## Slide 63: Modified Castigliano’s Theorem

## Slide 64: How about without P?

## Slide 65: Example

## Slide 66: Three-Point Bending

## Slide 67: Example

## Slide 68: Example

## Slide 69: Statically Indeterminate Beam

## Slide 70: Statically Indeterminate Beam

## Slide 71: Deflection by Loading Equation

## Slide 72: Assignment
Text book
6.2, 6.19, 6.22，6.47, 6.55, 6.69
Due April 22
6.168, 7.3, 7.10, 7.11, 12.10, 12.13, 12.23
Due April 29:
12.89, 12.91, 12.92, 12.103, 12.108, 14.14, 14-18, 14-155, 14-135, 14-138